About Yarrawonga Health

Yarrawonga Health is Moira Shire’s largest health service providing acute inpatient services, residential aged care and primary and community health services. The health service comprises 19 acute medical and surgical beds; two labour delivery rooms, a dedicated day-stay unit, three residential facilities onsite with a total of 88 beds, as well as an adjacent Community Health Centre.

About the project

A review by Yarrawonga Health in 2013 found that over the previous five years electricity consumption had remained relatively stable, but costs had risen by approximately 60 per cent. Electricity is predominantly used for air conditioning, ventilation and lighting.

In order to alleviate increasing energy costs, Yarrawonga Health with financial support from the Department of Health installed a 96 kilo-watt photovoltaic solar array. In addition, the department supported Yarrawonga Health with an LED lighting replacement project that is currently being implemented.

Figure 1: Photovoltaic solar array at Yarrawonga Health

Besides energy cost savings the system was chosen to reduce the organisation’s carbon emissions and demonstrate leadership in environmental management within the local community.

The anticipated benefits from the solar array were annual savings of $25,000 to $30,000 and an annual reduction of some 200 tonnes in carbon emissions.

The system consists of:

2 x 48 kW inverters

384 x 250 Watt solar panels

cabling and racking, isolators and circuit breakers

data logging and remote access, and

safety access walkways and anchor lines.

The project was planned and facilitated by Yarrawonga Health with assistance from a structural and an electrical engineer.

Results

Over the period 11 August 2013 to 31 January 2014 the project achieved the following outcomes, which suggest that the project will achieve the anticipated benefits:

a reduction of 87,543 kWh of purchased electricity from the grid as compared to the same period in the year before

generated solar electricity of 83,311 kWh, averaging 13,885 kWh per month

cost savings of $14,163, averaging $2,360 per month, or about 15 per cent reduction in electricity expenditure, and

carbon emission savings of 99.5 tonnes.

Additional electricity and carbon, and associated financial, savings are expected at Yarrawonga Health from the LED lighting project currently being implemented.

A related benefit from the project has been an ongoing organisational cultural change at Yarrawonga Health in relation to energy use. Staff have embraced the project and have a better understanding of energy efficiency and what they can do to reduce energy use.

Detailed results from the installation of the solar system are provided in the Appendix in a graphical format.

Further information

# James Flanagan

# Facility Manager

Yarrawonga Health

E. james.flanagan@yh.org.au

T. (03) 5743 8154

Further case studies on environmental sustainability can be found at www.health.vic.gov.au/sustainability.

April 2014

Appendix - Selected charts

Figure 2: Generated solar electricity and financial savings per month

Figure 3: Monthly site electricity consumption in kWh

# Text boxes

Solar photovoltaic project at Yarrawonga Health

Case Study